## Slide 1: TỔNG HỢP KIẾN THỨC VÀ CÔNG THỨC ANTEN
CẦN NHỚ ( ôn tập thi cuối kỳ)

## Slide 2: CHƯƠNG 1
Cơ chế bức xạ của Anten
1 dây
Nếu điện tích trên dây không chuyển động không có hiện tượng bức xạ sóng điện từ (EM)
Nếu điện tích di chuyển với tốc độ đều
  Không có hiện tượng bức xạ nếu dây thẳng và dài vô hạn
  Có hiện tượng bức xạ khi dây cong, gãy khúc, không liên tục hoặc bị giới hạn
Nếu điện tích dao động theo thời gian thì có hiện tượng bức xạ ngay cả khi dây dẫn thẳng

## Slide 3
Điện trường giữa hai dây làm cho các điện tích tự do trong dây dẫn di chuyển
Sự di chuyển tạo dòng diện thay đổi ( ở cuối dây dẫn) và do đó tạo ra điện trường và từ trường
Đặc tính của đường sức điện từ trường là:
  Bắt đầu ở điện tích dương và kết thúc ở điện tích âm
  Bắt đầu từ vô cùng và kết thúc ở điện tích âm
  Bắt đầu từ điện tích dương và kết thúc ở vô cùng
  Không bắt đầu từ điện tích âm cũng như điện tích dương và có dạng khép kín
Cơ chế bức xạ của Anten
2 dây

## Slide 4
Cơ chế bức xạ của Anten
Dipole:

## Slide 5
Dipole:
Sự chuyển động của điện tích tạo nên một sóng dòng điện trong dây dẫn
Sóng này sẽ bị phản xạ tại cuối dây dẫn
Sự kết hợp sóng đến và sóng phản xạ tạo ra sóng đứng
Dựa vào sự phân bố không gian + sự thay đổi theo thời gian tạo ra bức xạ sóng điện từ
Nếu là dây dẫn thẳng thì bức xạ điện từ trên dây dẫn sẽ triệt tiêu lẫn nhau
Cơ chế bức xạ của Anten

## Slide 6
Cơ chế bức xạ của Anten
Sự bức xạ sóng điện từ chỉ xảy ra khi từ trường do hai thanh dipole tạo ra được tăng cường lẫn nhau hoặc không triệt tiêu lẫn nhau

## Slide 7
Dipole:
Cơ chế bức xạ của Anten
Phân bố dòng theo thời gian đối với dipole

## Slide 8: CHƯƠNG 2
Xem Anten như mạng một cửa
Trở kháng vào: ZA = RA + jXA
Thông thường RA gồm 2 thành phần
+ Rr là điện trở bức xạ
+ RL là điện trở tiêu hao của Anten
Nếu có phối hợp trở kháng liên hợp ZA* = ZS

## Slide 9: CHƯƠNG 2
Trường điện từ bức xạ tạo bởi Anten
Trường điện từ ở vùng xa Anten có thể biểu diễn
Trong đó
là độ thẩm từ và điện trong KGTD
r là khoảng cách từ Anten đến điểm khảo sát
D là đường kính hình cầu ngoại tiếp Anten
Điều kiện vùng xa: r>>D, r>>, r>>

## Slide 10: CHƯƠNG 2
Mật độ dòng công suất của trường bức xạ [W/m2]
Góc khối Anten
Cường độ bức xạ là công suất bức xạ trên một đơn vị góc khối

## Slide 11
Công suất bức xạ
Điện trở Rr của Anten
CHƯƠNG 2
Cường độ bức xạ chuẩn hoá và hàm độ lớn của trường như sau
Góc khối của Anten

## Slide 12
cường độ bức xạ trung bình
Độ định hướng:
CHƯƠNG 2
Hệ số định hướng

## Slide 13
Độ lợi Anten được định nghĩa
Độ lợi công suất (là độ lớn cực đại của độ lợi Anten)
Cường độ công suất
Công suất hấp thụ của Anten
Hiệu suất của anten
Độ lợi hướng tính
CHƯƠNG 2

## Slide 14
EIRP (Equivalent Isotropically Radiated Power)
CHƯƠNG 2
  mật độ công suất trung bình trong mặt phẳng tới
vector phân cực liên quan đến sóng tới
  Công suất anten thu
Diện tích hiệu dụng của Anten

## Slide 15
Pt = PRad Công suất anten phát
Gt Độ lợi công suất anten phát
Dt Độ lợi định hướng anten phát
et Hiệu suất anten phát
Γt Hệ số phát xạ anten phát
Tuyến Anten

## Slide 16
Gọi Ar là diện tích hiệu dụng của anten thu:
Tỷ lệ công suất thu và công suất phát ra là:
(1)
Tuyến Anten
Công suất thu
(2)
(3)
D = Gmax = G0
Công thức (1), (2), (3) còn được gọi là công thức truyền dẫn Friis (Friis Transmission Equation)

## Slide 17: CHƯƠNG 3
Các phương trình Maxwell :
Dạng tích phân | Dạng vi phân
ò
ò
ò
+
=
S
S
C
dS
D
dt
d
dS
J
dl
H
r
r
r
ò
ò
-
=
S
C
dS
B
dt
d
dl
E
r
r

## Slide 18: CHƯƠNG 3
Mật độ thông lượng điện [C / m2]
Mật độ thông lượng từ [T] [Tesla] [Weber / m2 ]
Mật độ dòng điện [A / m2 ]
Mật độ điện tích [C / m3]
E Điện trường (V/m)
H Từ trường (A/m)
Toán tử Gradient , Nabla, Hamilton
continuity law
Ohm law
Phương trình Maxwell trong không gian tự do:

## Slide 19: CHƯƠNG 3
Từ pt Maxwell ta đã chứng minh được sự tồn tại của A và Φ.
Vectơ từ thế A được cho bởi:
Thế vô hướng điện Φ được cho bởi:
Khi A và Φ được xác định, ta có:
Vector A có đơn vị của dòng điện (Ampere) và Scalar (Φ) có đơn vị điện thế (volts).
Sử dụng điều kiện lorentz ta có:

## Slide 20: CHƯƠNG 3
Miền thời gian
Miền tần số
Vector từ thế (Vector potential wave equation) Và thế vô hướng
Trong tĩnh điện học, phương trình Poisson có dạng
Trong phương trình sóng thế vô hướng có dạng

## Slide 21: CHƯƠNG 3
Trong từ tĩnh học, phương trình vector Poisson có dạng:
Nghiệm phương trình vector Poisson:
Phương trình sóng từ vector (A) (Magnetostatics)
Phương trình sóng từ thế vector

## Slide 22: CHƯƠNG 3
Xét A Point Source tạo thành dòng Jz trên trục z
The field produced by a unit point current is known as a Green function. This result will be used for all other sources.
(1) N points closed to the origin:
(2) Line source p(z) = I(z)dz on z axis:
(3) A volume source:

## Slide 23: CHƯƠNG 3
Idl
z
A
Xét A Short Current Filament tạo thành Idl trên trục z
Xét Far feild

## Slide 24
Hertzian Dipole Antenna

## Slide 25: Chương 4
Khái niệm dãy Anten
Tröôøng böùc xaï ôû vuøng xa laø:
Khi xeùt bieân ñoä:
β là sự khác pha giữa các elements
Array 2 phần tử dipole chiều dài hữu hạn đặt ngang theo trục Oz (trong mặt phẳng z0y)

## Slide 26
kích thích bôûi doøng ñieän gioáng nhau veà pha vaø bieân ñoä
Hệ thống bức xạ tử thẳng cách đều LUEESA
Moãi phaàn töû ñaúng höôùng
Bieân ñoä doøng ñieän kích thích ñeàu
Ñoàng pha  = 0

## Slide 27


n=1,2,3… N …
Khi n = 0, N, 2N, 3N, … mN … AF ñaït cöïc ñaïi.
m = 0,1,2,3…
Trong thöïc teá chuû yeáu xeùt goùc leäch pha ψ bieán ñoåi töø 0 ñeán 2π.
Xaùc ñònh nhöõng ñieåm NULL cuûa array:
Hệ thống bức xạ tử thẳng cách đều

## Slide 28
=> Haøm cuûa Ψ
Nhận xét:
Cực đại xuất hiện tại Ψ = 0
Hàm có chu kỳ 2π. Đối xứng xung quanh Ψ = π.
Có N-1 Null có khoảng cách bằng nhau và cách nhau 2π/N (0<Ψ<2π)
Có N-2 Sidelopes có độ rộng 2π/N.
Tại gốc toạ độ có búp sóng chính rộng 4π/N
Hệ thống bức xạ tử thẳng cách đều

## Slide 29
Xác định số chấn tử N
Vẽ nửa vòng tròn bán kính kd có tâm tại Ψ = β
Chiếu từ đồ thị sắp xếp xuống đường tròn vừa vẽ
Vẽ đồ thị hệ số giàn theo nguyên tắc đã nêu
Lấy đối xứng quanh trục hoành (chính là Oz)
Hệ thống bức xạ tử thẳng cách đều

## Slide 30: Chương 5
Anten xoắn Helix – Helical Antenna

## Slide 31
Introduction
Broadband dipole antennas were discussed at the beginning of this chapter
There are numerous other antenna designs that exhibit greater broadband characteristics than those of the dipoles
Some of these antenna can also provide circular polarization
A desired extra feature for many applications
Another basic, simple, and practical conﬁguration of an electromagnetic radiator is that of a conducting wire wound in the form of a screw thread forming a helix
Anten xoắn Helix – Helical Antenna

## Slide 32
Introduction
Anten xoắn Helix – Helical Antenna
Helical antenna with ground plane
The geometrical conﬁguration of a helix consists usually of:
N turns
diameter D
and spacing S between each turn
The diameter of the ground plane should be at least 3λ/4

## Slide 33
Introduction
Anten xoắn Helix – Helical Antenna
Helical antenna with ground plane
The total length of the antenna: L = NS
The total length of the wire:
is the length of the wire between each turn
C = πD is the circumference of the helix
The pitch angle α

## Slide 34
Introduction
Anten xoắn Helix – Helical Antenna
When α = 0◦, the helix reduces to a loop antenna of N turns
When α = 90◦, then the helix reduces to a linear wire
When 0◦<α< 90◦, then a true helix is formed !
The radiation characteristics can be varied by controlling the size of its geometrical properties compared to the wavelength
The input impedance is critically dependent upon the pitch angle and the size of the conducting wire
The general polarization of the antenna is elliptical
However circular and linear polarizations can be achieved over different frequency ranges

## Slide 35
Operation
Anten xoắn Helix – Helical Antenna
The helical antenna can operate in many modes
The two principal ones are the normal (broadside) and the axial (end-ﬁre) modes
Three-dimensional normalized amplitude linear power patterns

## Slide 36
Operation
Anten xoắn Helix – Helical Antenna
Normal Mode: has three-dimensional amplitude patterns maximum in a plane normal to the axis and is nearly null along the axis
Axial mode: has its maximum along the axis of the helix, and it is similar to that of an end-ﬁre array
The axial (end-ﬁre) mode is usually the most practical because it can achieve circular polarization over a wider bandwidth and it is more efficient

## Slide 37
Normal Mode
Anten xoắn Helix – Helical Antenna
To achieve the normal mode of operation, the dimensions of the helix are usually small compared to the wavelength
NL0 << λ0
The geometry of the helix reduces to a loop of diameter D when the pitch angle approaches zero and to a linear wire of length S when it approaches 90◦
The limiting geometries of the helix are a loop and a dipole

## Slide 38
Normal Mode
Anten xoắn Helix – Helical Antenna
The far-zone electric ﬁeld radiated by a short dipole of length S and constant current I0 is Eθ (where l is being replaced by S)
The electric ﬁeld radiated by a loop is Eφ (where D/2 is substituted for a)

## Slide 39
Normal Mode
Anten xoắn Helix – Helical Antenna
The ratio of the magnitudes of the Eθ and Eφ components is deﬁned as
There are 3 special cases:
when leading to a linearly polarized wave of horizontal polarization (the helix is a loop)
AR =∞, Eφ = 0: the radiated wave is linearly polarized with vertical polarization (the helix is a vertical dipole)

## Slide 40
Normal Mode
Anten xoắn Helix – Helical Antenna
There are 3 special cases:
AR = 1 when or
When the dimensional parameters of the helix satisfy the above relation, the radiated ﬁeld is circularly polarized in all directions other than θ = 0◦ where the ﬁelds vanish

## Slide 41
Normal Mode
Anten xoắn Helix – Helical Antenna
Conclusion
Because of the critical dependence of its radiation characteristics on its geometrical dimensions, which must be very small compared to the wavelength, this mode of operation is very narrow in bandwidth and its radiation efﬁciency is very small. Practically this mode of operation is limited, and it is seldom utilized

## Slide 42
Axial Mode
Anten xoắn Helix – Helical Antenna
There is only one major lobe and maximum radiation intensity is along the axis of the helix. The minor lobes are at oblique angles to the axis
To excite this mode, D và S >> 
To achieve circular polarization,
Circumference: (with C/λ0 = 1 near optimum)
The spacing:
The pitch angle is usually 12◦ ≤ α ≤14◦

## Slide 43
Axial Mode
Anten xoắn Helix – Helical Antenna
Conclusion
Most often the antenna is used in conjunction with a ground plane, whose diameter is at least λ0/2, and it is fed by a coaxial line. However, other types of feeds (such as waveguides and dielectric rods) are possible, especially at microwave frequencies. The dimensions of the helix for this mode of operation are not as critical, thus resulting in a greater bandwidth

## Slide 44
Design Procedure
Anten xoắn Helix – Helical Antenna
Input impedance: R = 100÷200  ohms
Empirical expressions:
Input impedance: accurate to about ±20%
The half-power beamwidth:
The beamwidth between nulls:

## Slide 45
Design Procedure
Anten xoắn Helix – Helical Antenna
Input impedance: R = 100÷200  ohms
Empirical expressions:
The directivity:
The axial ratio:

## Slide 46
Design Procedure
Anten xoắn Helix – Helical Antenna
Empirical expressions:
The normalized far-ﬁeld pattern:
All these relations are approximately valid provided 12◦<α< 14◦, 3/4 < C/λ0 < 4/3, and N > 3
where

## Slide 47
Design Procedure
Anten xoắn Helix – Helical Antenna
Example 1:
Design a 10-turn helix to operate in the axial mode. For an optimum design. Determine the:
a. Circumference (in λ0), pitch angle (in degrees), and separation between turns (in λ0)
b. Relative (to free space) wave velocity along the wire of the helix for:
i. Ordinary end-ﬁre design
ii. Hansen-Woodyard end-ﬁre design

## Slide 48
Design Procedure
Anten xoắn Helix – Helical Antenna
Example 1:
Design a 10-turn helix to operate in the axial mode. For an optimum design
c. Half-power beamwidth of the main lobe (in degrees)
d. Directivity (in dB) using a formula
e. Axial ratio (dimensionless and in dB)

## Slide 49
Design Procedure
Anten xoắn Helix – Helical Antenna
Solution:
a. Circumference (in λ0), pitch angle (in degrees), and separation between turns (in λ0)
For an optimum design:
⇒ S = C.tanα = λ0.tan(13◦) = 0.231λ0
b. Relative (to free space) wave velocity along the wire of the helix for:
i. Ordinary end-ﬁre design
ii. Hansen-Woodyard end-ﬁre design

## Slide 50
Design Procedure
Anten xoắn Helix – Helical Antenna
Solution: b. The length of a single turn is:
Therefore the relative wave velocity is
Ordinary end-ﬁre
ii. Hansen-Woodyard end-ﬁre:

## Slide 51
Design Procedure
Anten xoắn Helix – Helical Antenna
Solution:
c. The half-power beamwidth:
d. Directivity (in dB) using a formula:

## Slide 52
Design Procedure
Anten xoắn Helix – Helical Antenna
Solution:
e. The axial ratio: